## Slide 1: Introduction to Single-Board Computers and Microcontrollers
Or: The difference between
Arduino and Raspberry Pi
and alternatives

## Slide 2: Single-Board Computer vs. Microcontroller
Arduino UNO
Microcontroller (MCU)
Raspberry Pi
Single-Board Computer

## Slide 3: Outline
Introduction: Why they are popular
Characteristics
Two main skillsets required
Single-board computer vs microcontroller:
  When to use which?
  Different Types of Microcontrollers
  Different Types of Single-board Computers

## Slide 4: About Me
Vision-based robot control
UBCO Mechatronics Club
Time-Lapse Photography

## Slide 5: My Knowledge about Arduino/RPi
http://edisondev.net/
  Tutorials and information about single-board computers and microcontrollers
  “Late”st News

## Slide 6: What can you do with Arduinos or Raspberry Pis?
Jasper – Voice Controller powered by Rpi https://jasperproject.github.io
LED Cube - http://www.instructables.com/id/Led-Cube-8x8x8/
Flamethrower Jack-O-Lantern - http://www.instructables.com/id/Flamethrowing-Jack-O-Lantern/
Arduino RC- Lawnmower http://www.instructables.com/id/Arduino-RC-Lawnmower/
Fermentation Monitoring - https://www.sparkfun.com/tutorials/131
Raspberry Eye - https://hackaday.io/project/865-raspberry-eye

## Slide 7: Why are they so popular?
They are cheap
They sense and manipulate the physical world
  GPIO pins (reading values/sending instructions)

## Slide 8: Internet of Things (IoT)
Connection of embedded computing devices to the internet
  Home Automation
  Augmented Reality
Connecting non-computer devices
  Aquariums
  Home Entertainment
  Etc.

## Slide 9: Single-Board Computer vs. Microcontroller What is the difference?
Microcontrollers
Single-board Computers

## Slide 10: Single-Board Computer vs. Microcontroller What is needed for a Computer/Microcontroller?
Processor
Storage
RAM
Notes: Processor: Executes instructions

## Slide 11: Single-Board Computer vs. Microcontroller Rough Specifications
 | Microcontrollers | Single-Board Computers
Processor Speed | ~50 Mhz | 1 Ghz +
Onboard Storage | 64 Kb | Flash, SD cards ~Gb
Memory (RAM) | 64 Kb | ~ 1 Gb
Power Consumption | 12 mA (2200 mAh battery -> 183hr) | 500 mA+ (2200 mAh battery-> 4.4 hr)
Reboot Time | <1 sec | ~ Multiple seconds
Other Features |  | Operating system Extendable Storage Network Connection

## Slide 12: Single-Board Computer vs. Microcontroller Examples of Embedded Systems
Image Source
http://pixshark.com/raspberry-pi-model-b-schematic.htm
http://images.studica.com/images/product/arduino/9a9b5c9e479e1a5b237b41a173d34dcfimage472x354_72_200x.gif
Broadcom BCM2835
CPU, GPU, RAM
Storage
ATMega328
CPU, RAM, Storage

## Slide 13: Single-Board Computer vs. Microcontroller Defining Features
Single-board computer
  Lots of processing power
  Has operating system (Linux, Android, soon Windows)
  Monitor Connection
  Cheap, “weak” computer
Microcontroller
  Devoted to having GPIO pins
  Low power, quick boot
  Very cheap (especially if you buy only IC)

## Slide 14: Challenges for Beginners
Working with these devices boils down to:
Image Source: https://openclipart.org/
Programming
Electronics Knowledge

## Slide 15: First Challenge Programming
Loads of Examples from Community
  With little skill you can program an Arduino to do simple things
But how do you write a program to control a robot arm?
  Mathematics
  Kinematics
  And other things you learn in school
  Need knowledge from diverse fields
Notes: Population is becoming more digitally literate

## Slide 16: First Challenge Programming – Simplifying Aspects
Pre-written Libraries
Code Examples
  https://github.com/
Community help (Forums, StackExchange)
Free online courses
  Search for “MIT Arduino Course”
  Programming courses on:
    Khan Academy
    Coursera
    Udacity

## Slide 17: Second Challenge Electronics – the hard part
Difficult to get started
Easy to make mistakes
  Some mistakes cannot be undone
Often needs additional equipment:
  Soldering Iron
  Voltmeter
  Oscilloscope

## Slide 18: Electronics Simplifying Aspects
Starter Packs and Kits
  Contain a minimum number of electronic components that you may need
Microcontroller Attachments
  Shields (for Arduino)
    Motor shields, sensor shields
  Capes (for Beagleboard)
  BoosterPacks (TI LaunchPad)
Notes: -Simplify things for beginners and prototyping
-Somewhat pricey
-You would not use it for the final product, because it has components that you don’t need

## Slide 19: Electronics Simplifying Aspects
A lot of electronics come like this:
Solution: Breakout boards: pre-soldered breadboard-ready electronics:
Source:
http://elecshop.blog.com/files/2014/01/313-44-TQFP.jpg
http://www.renesas.com/media/press/news/2010/20101006.jpg

## Slide 20: Electronics Simplifying Aspects
Community
  People who know things and are willing to share
  Accessible tutorials
http://xkcd.com/979/
Notes: -Simplify things for beginners and prototyping
-Somewhat pricey
-You would not use it for the final product, because it has components that you don’t need

## Slide 21: Microcontroller Microcontroller vs. Expansion Boards
Microcontrollers:
Expansion Board:
Image Source: http://en.wikipedia.org/wiki/Microcontroller

## Slide 22: Microcontroller Microcontrollers Features
Processor Speed (Mhz)
RAM
On-board storage (FLASH)
GPIO Pins
Analog to Digital Converters (ADC)
Logic Level Voltage (3.3V or 5V)

## Slide 23: Microcontroller Expansion Board Features
Communication Cable Attachments
Programmer
Buttons
Power Supply Connectors
Pin connectors
On-board Sensors
  (accelerometers, real-time clocks, temperature sensors)

## Slide 24: Microcontroller Arduino UNO Board Diagram
Source: http://arduino-info.wikispaces.com/file/view/Arduino_Uno_Rev3-schematic.jpg/346644662/Arduino_Uno_Rev3-schematic.jpg
Arduino ATMEGA328P
USB Interface + Programmer

## Slide 25: Microcontrollers Arduino
 | Arduino Uno | Arduino Mega2560 | Arduino Nano (ATmega328)
Microcontroller | ATmega328 | ATmega2560 | ATmega328
Flash Memory | 32KB | 256KB | 32KB
Clock Speed | 16MHz | 16MHz | 16 MHz
RAM | 2KB | 8KB | 1KB
Price (approx, USD) | $24.95here | $45.95 here | $34.99 here
Digital I/O Pins | 14 | 54 | 14
http://arduino.cc/

## Slide 26: Microcontrollers Arduino IDE - Programming
http://arduino.cc/

## Slide 27: Microcontrollers STM Microcontrollers
 | STM32L DISCOVERY | STM32 Nucleo F401RE
Microcontroller | STM32L152RBT6 Cortex-M3 CPU | STM32F401RET6
Flash Memory | 128KB | 2 MB
Clock Speed | 32 Mhz | 180 Mhz
RAM | 16KB | 256 KB
Price (approx, USD) | $10.50 here | $12.40 here
Other | 1 touch sensor 1 LCD display | 
http://www.st.com/web/catalog/tools/PF250990

## Slide 28: Programming Any Microcontroller
Eclipse https://eclipse.org/

## Slide 29: Microcontrollers Texas Instruments LaunchPad
 | MSP-EXP430G2 | MSP430F5529 | Tiva C Series TMC4C1294
Microcontroller | MSP430 | MSP430 | TM4C1294NCPDT ARM Cortex-M4
Flash Memory | 16 KB | 128KB | 1 MB
Clock Speed | 16 Mhz | 25 MHz | 120 Mhz
RAM | 512B | 8KB | 256 KB
Price (approx, USD) | $9.99 here | $12.99 here | $19.99 here
Other |  |  | Ethernet
http://www.ti.com/ww/en/launchpad/launchpad.html

## Slide 30: Microcontrollers LaunchPad Programming
Code Composer Studio
Energia
http://energia.nu/

## Slide 31: Microcontrollers Thousands Others
Beetle
Nanode
Pinguino PIC32
Ruggeduino
Gamebuino
Some of these had limited production runs or have been discontinued.
Freescale Freedom
Teensy
Beetle: http://www.dfrobot.com/wiki/index.php/Beetle_SKU:DFR0282
Nanode: http://www.nanode.eu/
Pinguino PIC32: https://www.olimex.com/Products/Duino/PIC32/PIC32-PINGUINO/open-source-hardware
Ruggeduino: http://www.ruggedcircuits.com/ruggeduino/
Gamebuino: http://gamebuino.com/
Freescale Freedom: http://www.freescale.com/webapp/sps/site/overview.jsp?code=FREDEVPLA
Teensy: https://www.pjrc.com/teensy/

## Slide 32: Single-Board Computers
Properties
  Processor Speed (Ghz, Multiple core)
  RAM (speed of RAM)
  Video Card (Home entertainment)
  On-board storage (FLASH)
  Hard-drive storage
  GPIO pins
  Features
    Audio jack
    IR remote
    Blue tooth
    Other connectors

## Slide 33: Single-Board Computers Hidden Costs
Minimum:
Other Requirements:
SD card
Ethernet Connection
USB Power
HDMI connection + Monitor
Keyboard + Mouse +
USB Hub (sometimes)

## Slide 34: Single-Board Computers Raspberry Pi
 | Raspberry Pi Model B | Raspberry Pi 2
Processor | ARM1176JZF-S core | Quad-core ARM7
Flash Memory | None | None
Clock Speed | 700 MHz | 800 MHz
RAM | 512MB | 1 GB
Price (approx, USD) | $39.95 | $35.00
Other Features | 2x USB ports 26x GPIO pins | 4x USB2.0 40x GPIO pins
Image Source: http://www.techradar.com/news/computing-components/peripherals/raspberry-pi-2-outed-with-faster-cpu-double-ram-and-windows-10-support-1283075
http://www.raspberrypi.org/

## Slide 35: Single-Board Computers Beaglebone Black
 | Beaglebone Black
Processor | 1GHZ
Flash Memory | 2GB 8-bit eMMC on-board storage
RAM | 512MB DDR3
Other Features | Open Hardware Architecture 1x USB port 92x GPIO pins
Price (approx, USD) | $45.00
http://beagleboard.org/

## Slide 36: Single board Computers Banana Pi
 | Banana Pi
Processor | 1 GHz dual core
Flash Memory | None
RAM | 1GB DD3
Other Features | SATA Connection Audio Connector 2x USB
Price (approx, USD) | $60
http://www.bananapi.org/

## Slide 37: Single board Computers ODROID-C1
 | ODROID-C1
Processor | 1.5GHz quad core
Flash Memory | slot for expansion
RAM | 1GB DD3
Other Features | Infrared (IR) receiver 4x USB
Price (approx, USD) | $36.95
http://www.hardkernel.com

## Slide 38: Single-Board Computers UDOO
 | UDOO Quad
Processor | Quad-core 1GHz
Flash Memory | None (SATA connector)
RAM | 1 GB DDR3
Other Features | 2x USB port WiFi Module 76 x GPIO pins Analog Audio and Mic
Price (approx, USD) | $135.00
http://www.udoo.org/

## Slide 39: Single board Computers Firefly-RK3288
 | Firefly-RK3288
Processor | 1.8GHz quad core
Flash Memory | 16 GB
RAM | 2 GB DD3
Other Features | Infrared (IR) receiver VGA adapter 2x USB
Price (approx, USD) | $189
http://www.t-firefly.com/en/

## Slide 40: Conclusion
Community is Key
  If you learn something, share.
Don’t just stick to the “popular” devices.
For low power requirements, simple tasks, use microcontroller.